## Slide 1: Boolean Algebra Digital Logic Computer Org. & Arch. Computer Operating Systems

## Slide 2: Objectives
In this lecture, you will learn basic concepts about
Boolean algebra
Digital logic gates
Digital logic circuits
Computer organization & architecture
Computer operating systems

## Slide 3: Boolean Algebra

## Slide 4: Boolean Algebra
Introduced by George Boole (1815-1864), British mathematician and philosopher
In general, an algebra over finite sets of discrete values
Variables can have values of either 0 (false) or 1 (true).
Fundamental in today’s digital computing.

## Slide 5: Boolean Variables/Values
A Boolean variable can be either 1 (true) or 0 (false).
Boolean algebra is operating over these Boolean values.

## Slide 6: Boolean Operators
Relational operators (<, <=, ==, >, >=, and !=),
Logic AND, OR, NOT
  Notations used for AND is a period (.) or nothing like
  Notations used for OR is a plus sign (+) like
  Notations for NOT like

## Slide 7: Operator Precedence
Dictate which operation will perform first
Precedence Order Decreases

## Slide 8: Boolean Expression
A Boolean expression can be the following
A Boolean variable,
A relational expression, or
Any combination of Boolean variables, relational expressions, and Boolean expressions with logical operators AND, OR, NOT, and parentheses.

## Slide 9: Boolean Functions
A Boolean function maps a set of Boolean variables to a Boolean value.
Consider
Boolean variables A, and B can only hold 0 or 1. The operator “+” denotes an OR.
So, the Boolean function represents logical OR.

## Slide 10: Truth Table
A visual representation of a Boolean function.
Input variables to the left, and an output to the rightmost
All possible input values (combinations) are listed.
Normally, they are listed in ascending order.
A | B | f(A,B)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 11: Laws of Boolean Algebra
Like regular algebra, there are laws in the Boolean algebra that ease the computation, or simplify Boolean expressions.
Some of the laws from regular algebra may NOT apply to Boolean algebra.
Examples:
  Distribution law
  Inverse law
  Commutative law

## Slide 12: Laws of Boolean Algebra
More example laws:
  Associative law
  Identity law
  Redundance law
  False law
  True law
  De Morgan’s law

## Slide 13: Boolean Expression Simplification
Consider A+AB
Actually, A+AB=A
Consider
Actually,
We can apply Boolean Algebra laws to simplify expressions.
  Key to design efficient digital circuits

## Slide 14: Digital Logic Gates

## Slide 15: 2-Input Boolean Functions
A | B | f(A,B)
0 | 0 | ?
0 | 1 | ?
1 | 0 | ?
1 | 1 | ?

## Slide 16: AND
Boolean function f(A, B) is true only if both A and B are true. f(A, B)=AB
AND function is also called Boolean product.
A | B | f(A,B)
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 17: OR
Boolean function f(A, B) is false only if both A and B are false. f(A, B)=A+B
OR function is also called Boolean sum.
A | B | f(A,B)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 18: NOT
Boolean function f(A) is true only if A is false.
NOT function is also called Boolean inverse.
A | f(A)
0 | 1
1 | 0

## Slide 19: Exclusive OR (XOR)
Boolean function f(A, B) is true only if one of A and B is true, not both.
A | B | f(A,B)
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 20: NAND
Not AND
A | B | f(A,B)
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 21: NOR
Not OR
A | B | f(A,B)
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 22: Gate Symbols
Symbols that represent electronic circuits for gates
not

## Slide 23: Transistor Implementation
Transistors are used to implement logic gates.
E.g., NOT gate

## Slide 24: Characteristics of Gates
Outputs are subject to inputs only.
Switching time form on to off, or off back to on, takes a few nanoseconds in transistors.
Propagation delay from inputs to outputs refers to the time between the inputs change and the new reflected outputs.
Gate delay refers to the propagation delay for a gate.

## Slide 25: Computational Completeness
Any Boolean function can be computed using one type of computationally complete gates.
NOR and NAND are computationally complete gates.
They are easily to be manufactured than others.
Normally, you have a pack of NANDs in an IC. You want to reuse them as many as possible to save cost and space.

## Slide 26: Equivalent NOT

## Slide 27: Equivalent AND

## Slide 28: Equivalent OR

## Slide 29: Logic Gate Equivalence
Invert the inputs
Exchange AND and OR
Invert the output

## Slide 30: Digital Logic Circuits

## Slide 31: Digital Computation
Boolean algebra deals with operations over binary digits and generates binary results.
Arithmetic operations can be described by truth tables.
Truth tables can be converted to Boolean expressions.
Digital circuits can be built based on Boolean expressions (sum or product).

## Slide 32: Combinational Logic
The output of a logic circuit depends only on its inputs.
E.g., the full adder
It is called combinational logic, combinational circuit, or combinatorial logic.
Combinational logic does not remember its previous state.

## Slide 33: Combinational Logic Design
Find out what are inputs and what are outputs
Build truth tables
Derive Boolean functions
Simplify Boolean functions
Create the circuit

## Slide 34: Example: Half Adder
Truth table and Boolean function

## Slide 35: Example: Half Adder
Logic circuit

## Slide 36: Example: Full Adder

## Slide 37: Example: 1-Bit ALU

## Slide 38: Sequential Logic
Outputs of sequential logic are based on inputs and its current internal state.
Usually, sequential logic circuit involves clock, which triggers state transition.
Sequential logic: Latch, Flip-Flop, Registers, Memory, etc.

## Slide 39: Example: Latch
The most basic sequential logic
Can keep (or, remember) one bit of information
No clock involved

## Slide 40: Clocks
(a) A clock. (b) The timing diagram for the clock.
(c) Generation of an asymmetric clock.
Every computer contains at least one clock that:
  Regulates how quickly instructions can be executed
  Synchronizes the activities of its components.
A fixed number of clock cycles are required to carry out each data movement or computational operation.

## Slide 41: Example: D Flip-Flop
A flip-flop is a latch triggered by a rising edge or a falling edge of the clock.
Symbols for D flip-flops

## Slide 42: Example: Registers
Registers are groups of flip-flops, where each flip-flop is capable of storing one bit of information.
Normally, 8-bit/16-bit/32-bit/64-bit registers
Store data in CPU for computation
Can also be used to build memories

## Slide 43: Example: Registers
An 8-bit register constructed from single-bit flip-flops

## Slide 44: Density of Integrated Circuit
SSI
  Small-scale integration packages gates
  Dozens of gates per chip
MSI
  Medium-scale integration packages functions, e.g. adders, multiplexors
  Hundreds of gates per chip
LSI
  Large-scale integration packages complete units, e.g. a calculator chip
  Thousands of gates per chip
VLSI
  Very large-scale integration packages complex units with millions of transistors.

## Slide 45: Computer Organization & Architecture

## Slide 46: Basic Structure of Computers
Coded info is stored in memory for later use
Input unit accepts code info from human operators, electromechanical devices (ie keyboard), other computers via networks
ALU uses the coded info to perform the desired operations
The output unit sends the results back out externally
Program is stored in memory and determines the processing steps
All actions are coordinated by the control unit
Collectively called the I/O unit
Collectively called the processor
The von Neumann Architecture

## Slide 47: The Bus
Buses consist of data lines, control lines, and address lines.
Data lines convey bits from one device to another. Move the actual information that must be moved from one location to another.
Control lines determine the direction of data flow, and when each device can access the bus.
Address lines determine the location of the source or destination of the data.

## Slide 48: CPU
Inside CPU
Outside Appearance (Top & Bottom)

## Slide 49: Memory
Computer memory consists of a linear array of addressable storage cells that are similar to registers.
x

## Slide 50: Motherboard

## Slide 51: Computer Operating Systems

## Slide 52: Definition
An Operating System (OS) is low-level system software that
  manages computer hardware and software resources;
  provides common services for computer programs to interact with computer hardware and other programs.
https://en.wikipedia.org/wiki/File:Operating_system_placement.svg

## Slide 53: OS Services
Program execution
  OS provides an environment where a user can run programs without having to worry about memory allocation or CPU scheduling.
I/O operations
  OS helps a user/program utilize input/output devices without knowing hardware details of the I/O devices.
File system manipulation
  OS provides an interface for a user/program to access and manage files and directorys.
Communication
  OS facilitates communication between processes to exchange information, whether the processes are running on the same computer or on different computers.

## Slide 54: OS Services
Error detection
  OS constantly checks for errors in CPU, I/O, memory, etc., and takes actions to ensure correct and consistent computing.
Resource allocation
  OS manages resources (memory, CPU, file storage, etc.) using schedulers for multi-user or multi-tasking environments.
Protection
  OS ensures that all access to system resources is controlled and authenticated.

## Slide 55: Common Operating Systems
Linux
Microsoft Windows
Apple macOS
Google Android
Apple iOS

## Slide 56: Summary
Boolean algebra
  Boolean variable, operators, function, truth table
Digital logic gates
  Six basic gates, symbols, and truth tables
Digital logic circuits
  Combinational logic, sequential logic
Computer Organization & Architecture
  The von Neumann architecture
Computer Operating Systems
  Functions, services

## Slide 57: Thank You!